## Slide 1: Radiation Dose Management in Computed Tomography
L11
Strategies for CT in Pregnant Patients
Material of the e-learning program
IAEA, 2017

## Slide 2: Objectives
Understanding risk of CT radiation exposure in pregnancy
Steps to cut unnecessary radiation dose from CT
  Appropriate indications
  Reduce scan length
  Optimize scan parameters
  Use of shielding

## Slide 3: Quantitative Measures
X-rays ionize atoms and molecules in human tissues by deposition of energy
  Absorbed dose: Quantity of energy deposited locally in an organ by radiation from any source
  Equivalent dose: Product of averaged absorbed dose in an organ and radiation weighting factor
  Effective dose: Sum of products of equivalent doses for irradiated tissues/organs and suitable tissue - weighting factor (risk estimate)

## Slide 4: Quantitative Measures of Radiation
 | Absorbed Dose | Effective Dose
Current SI Units | 1 grey (Gy) | 1 sievert (Sv)
Old Units | 100 rad | 100 rem
“Loose change” | 1 rad = 10 mGy | 1 rem = 10 mSv

## Slide 5: Average fetal doses from maternal CT exams
Extra-abdominal Mean fetal dose (mGy)
CT head < 0.01 (max. dose <0.01)
CT chest
Routine 0.2 (max. dose= 1)
Pulmonary Emboli 0.2 (max. dose= 1)
Coronary arteries 0.1
Abdominal CT
Routine abdomen 4
Routine abdo-pelvis 25.0 (max. dose= 79.0)
Routine pelvis 25.0 (max. dose= 79.0)
Abdominal aorta CTA 34
Stone protocol 10
ICRP 84, McCollough, Radiographics 07
Wagner , Medical Physics publications

## Slide 6: Ionizing Radiation: Effects
Ionizing radiation can occur from either direct or scattered external beams
Direct cellular (molecule in path of x-ray) or indirect (free radical production) effects
Embryonic and fetal effects include
  Mutagenesis
  Teratogenesis
  Carcinogenesis

## Slide 7: Dose threshold for fetal effects
Fetal dose < 100 - 200 mGy is not associated with measurable increase in non cancer fetal risks
Most radiological investigations are associated with doses much less than 100 mGy

## Slide 8: Radiation mutagenesis
  Include germ-line genes alteration and mutations, which can affect future generations
  Biological filtration: Affected cells are often filtered out of existence by the body!
  Mutagenesis in offspring of radiated patients has not been demonstrated in humans, although these effects have been seen in plants and animals at high doses
Biological effects of Ionizing Radiation (BEIR 5)

## Slide 9: Prevalence of Congenital Malformations without Radiation
Rate per 1000 live births
Any malformation 45.3
Major malformation 27.7
Minor malformation 17.9
Malformations of:
MSK 14.3
Genitourinary 9.2
Cardiovascular 8.0
Central nervous 5.3
MGH Perinatal Collaborative Project

## Slide 10: Radiation Teratogenesis
Gestation weeks Embryonic and Fetal Effects
First week Most sensitive period for prenatal death
Failure to implant and conceptus death
2 - 8 weeks Most sensitive period for IUGR
Embryo is also predisposed to teratogenesis
2 - 5 weeks Most sensitive period for small head size
Low Dose: Small head size
Higher doses: small head with severe MR
8 -15 weeks No severe teratogenesis except GU and organ hypoplasia (brain and testis)
Most sensitive period for severe MR
15 weeks - term No documented risk for teratogenesis
In most sensitive period of teratogenesis, no evidence of adverse effects < 100 - 200 mGy.

## Slide 11: Radiation and birth defects
Conceptus radiation dose | Child without malformations | Child will not develop cancer | Child without malformations and cancer
0 mGy | 96.00% | 99.93% | 95.93%
50 mGy | 95.90% | 99.51% | 95.43%
100 mGy | 95.80% | 99.07% | 94.91%

## Slide 12: Radiation and birth defects
Question: My patient had abdominal CT in first trimester of pregnancy. Will the child have malformations?
First estimate the radiation dose to conceptus
(Generally << 50 mGy: Let us say 10 mGy)
Answer: About 4-6% children have malformations in absence of radiation exposure (baseline risk). Radiation dose (when < 100 mGy) to conceptus has not been shown to significantly increase the risk of malformations above the baseline risk.

## Slide 13: Radiation Carcinogenesis
Slight rise in background leukemia rate from 3.6/10000 to 5/10000 after in utero dose to 1-2 mGy
While an association between risk for cancer and prenatal radiation exposure is not questioned, etiologic significance of radiation remains unresolved
Boice JD Jr, Miller RW. Teratology 1999

## Slide 14: When to do CT?
CT must be performed only if information is imp. for care and not obtainable by other means
Informed decision: Radiologist, Physician, Patient
Life threatening conditions: image without delay
Non-emergent: pregnancy testing–if uterus will get irradiated

## Slide 15: Use of CT in pregnancy
Golden Rule 1:
Use of CT for Appropriate indications in pregnancy must NOT be restricted.
Golden rule 2:
When possible and timely, try non-ionizing radiation or lower dose imaging tests in pregnancy.
Golden rule 3:
While more than necessary radiation should be avoided, use of less than necessary radiation resulting in suboptimal information content should be strongly discouraged!

## Slide 16: Common indications for CT in pregnancy
Chest CT:
Pulmonary embolism
Abdominal CT:
Renal colic
Appendicitis

## Slide 17: Strategies for CT Dose Optimization in pregnancy
Use AEC to adapt mAs to patient size
Use appropriate kV based on clinical indication
  Lower KV for CT pulmonary embolism than for kidney stones
Prefer wider beam collimation to improve dose efficiency
Use non-overlapping pitch (≥ 1:1 but not 0.5:1) to minimize motion artifacts
Restrict scan range to what is absolutely necessary
Use lead shielding (External scatter - decrease anxiety)
Give oral contrast agent for internal shielding - better!

## Slide 18: CT pulmonary embolism in pregnancy: The Algorithm
Suspicion of PE
Doppler US of bilateral lower limbs
Chest PA radiograph - Normal lungs: V:Q
Abnormal lungs: CTA chest w/o lower limbs
Pulmonary embolism excluded
Patel et al. Radiographics 2007
If Negative
If Negative
DVT +
PE +
Anticoagulate

## Slide 19: CT pulmonary embolism
Positive Doppler for DVT implies anticoagulation.
No CT is needed in this case.
First Consider Doppler for Deep Vein Thrombosis (DVT)

## Slide 20: CTPE in pregnancy: The Approach
Localizer radiographs
  Ensure good patient centering before acquiring localizer radiographs
  Low kV and low mA for localizer radiograph
  Do not acquire extra-long localizer into abdomen
  Prefer two localizers for adequate centering
Patel et al. Radiographics 2007

## Slide 21: CT pulmonary embolism in pregnancy: The Approach
Minimize motion artifacts in CT images
  Demonstrate breath-holding
  Practice breath-hold with patient
  Use fast gantry rotation time
  Use non-overlapping pitch
  Prefer wide beam collimation when slice thickness is not limited
  Shorten scan range:
    Exclude upper abdomen: Inferior limit to just below xiphoid process
    No pelvis or lower limb scanning
Avoid suboptimal contrast enhancement in pulmonary arteries
  Instruct patients to avoid Valsalva maneuver
  Use good contrast bolus timing technique
  Make sure risk of contrast extravasation is minimized with saline flush
  Make sure there is good intravenous access for contrast

## Slide 22: CT pulmonary embolism in pregnancy: The Approach
Use 80 - 100 kV for patients who have body mass index of < 30 kg/m2
Prefer AEC technique over fixed mA
Use iterative reconstruction (when available)
  To enable additional radiation dose reduction over FBP technique
On use of lead shielding
  Remember external scatter does not cause much radiation in CT
  Most radiation to conceptus results from direct radiation or from internal scattering from chest to abdomen
  External shielding does not protect against internal scatter but does decrease anxiety
  When using external shield make sure to wrap the shield all around the patient.
Prakash, Kalra et al. Investigative Radiology 2010

## Slide 23: Internal Shielding: Pregnancy
Use of barium based oral contrast agents for internal shielding of conceptus during CT pulmonary embolism.
  Barium sulphate up to 30% (3-400 ml) reduces internal scatter by about 91% which is equal to 1mm lead shield
  Internal shield is more effective than external shield in reducing radiation dose to the conceptus from chest CT.
  Slowly administer 1-2 glasses of Ba Sulphate on CT table.
  Always give water after barium to wash out barium from esophagus to avoid artifacts.
  Yousefzadeh et al. Radiology 2006
  !!! Although innovative and seemingly straightforward, this approach has only been validated in phantom study and not in live human subjects. Should site choose to implement this approach, they should exercise caution. It is important to remember that in pregnant patients undergoing chest CT, it is far more important to apply suitable scan parameters including appropriately short scan length in the first place.

## Slide 24: Administration of Barium to pregnant patient undergoing chest CT

## Slide 25: Kidney stones and pregnancy: Use and Radiation Dose
Low-dose CT for renal calculi is sufficient
CT is especially helpful as urinary tract often difficult to see with US or radiographs due to pregnant uterus
Fetal radiation doses of 4 - 7 mGy and of 8 - 12 mGy at 0 and 3 months of gestation from a renal stone CT with a relatively low tube current (160 mA)

## Slide 26: Kidney stones and pregnancy: Use and Radiation Dose
Localizer radiographs
  Use low mAs to acquire the localizer
  Ensure good patient centering prior to localizer
Use AEC over fixed mA
  Set image quality parameter at lower level to reduce dose compared to routine abdomen CT
  25-30 NI for GE, 100 reference mAs for Siemens
Reduce scan range (strict “borders”)
  Top of kidney to pubic symphysis
Less than or equal to 120 kV
Pitch greater than or near to 1
Wider beam collimation for greater dose efficiency
  For ex: 16 slice CT: 16 *1.25 > 16*0.625
When available apply iterative reconstruction technique to enable dose reduction

## Slide 27: CT for Appendicitis in Pregnancy
Suspected appendicitis
Ultrasound: Appendicitis & Differentials
MR or CT abdomen and pelvis
Patel et al. Radiographics 2007
Appendicitis +
Appendicitis +
Surgery
If Negative

## Slide 28: CT for Appendicitis
Same rules for localizer radiographs
as for kidney stones
Transverse CT images
Single phase only
NO Dual pass please
Restrict scan coverage
120 kV generally
Apply AEC
Non-overlapping pitch
Wider beam collimation
When available apply iterative reconstructions to enable additional radiation dose reduction

## Slide 29: Precautions for pregnant patients
There should be a sign in each radiology waiting area
“Notify technologist if you think you are pregnant.”
Before CT:
  Radiographers must ask each woman of childbearing age if she thinks she might be pregnant
Fetal dose must be minimized without affecting diagnostic image quality

## Slide 30: Estimation and documentation of fetal exposure
Technologist should notify appropriate radiologist when imaging is performed on a pregnant patient
Radiation safety officer/medical physicist should estimate and document fetal radiation dose
Referring physician and patient must be advised about fetal exposure

## Slide 31: Assurance and Counseling
Inform patients
Dose information must be conveyed to physician to counsel pregnant patient and to help make informed decision regarding possible impact of radiation
MGH consent form

## Slide 32: Summary: CT in Pregnancy
There is no evidence that CT radiation doses are associated any measurable increase in miscarriage, prematurity, still-birth, mental retardation, or congenital anomalies.
An increase in lifetime risk of radiation-induced childhood cancer or leukemia cancer following in utero radiation.
Appropriateness is the most important parameter for use of CT in pregnancy.